GALAXY R-6

REGENERATIVE AIR STREET SWEEPER

- Full featured, highly versatile regenerative air street sweeper.

- Mounted on a tight turning NON-CDL 26,000 GVWR chassis.

- Large 6.12 yd3 STAINLESS STEEL hopper.

- Exclusive bolt together hopper panels – no welds.

- 5 year factory “no rust-through” hopper warranty.

- Deep cleaning - BLAST ORIFICE – style pick-up head.

- Up to 11’ sweeping path w/deep gutter cleaning 54” brooms.

- Top access door makes screen clean out quicker, safer, & easier.

- Spring balanced gutter brooms auto compensate for wear.

- 330 gallon dust suppressing water system.

Galaxy R-6XL Added Value Features

INCREASED PRODUCTIVITY/PERFORMANCE FEATURES

- NO CDL REQUIRED.  Mounted on 26,000 GVWR chassis.  Reduces your labor costs and make manpower scheduling easier.

- 80.5” BLAST ORIFICE style pick-up hood concentrates and directs impeller generated air to blasts stubborn debris from surface with hurricane force like winds.  Creates a swirling vortex or “horizontal tornado” along entire pick-up head for optimum cleaning/pick-up performance.

- Large 6.12 yd3 NON-MAGNETIC STAINLESS STEEL hopper minimizes dump cycles & maximizes sweeping productivity.  Larger/deeper hopper cavity aids in dust/air separation and ensures better dust control.

- Special HOODS UP “LITTER GULPER” feature ensures quick and effective loading of bulky, light litter.  Hood front rises to more easily vacuum in bulky debris build-ups.  Reduces possibility of clogging and ensures consistent one pass sweeping.

- Solidly mounted pick-up head SWEEPS IN FORWARD & REVERSE.  Eliminates need for wasteful, time consuming and potential unsafe second passes over stubborn debris.  Reverse sweeping maximizes safety and productivity.

- Oversized 28 ft2 stainless steel debris separator screens resist clogging.  Screens are easily cleaned from outside of unit via top access hopper door.  Better air flow means more sweeping with fewer hopper dumps.

- Top mounted hopper door OPENS AUTOMATICALLY during dumping cycle.  Provides for safer, quicker, more hassle-free cleaning of stainless steel screens and hopper.   No need to climb inside hopper to clean/inspect.  The cleaner the screens, the better the sweeping performance.  Hopper dump height is 38”.

- 2 opposite positioned, stainless steel OVERSIZED 13.7”x26” hopper inspection doors aid in bulk debris loading and hopper cleaning.

- 10’ sweeping path with 42” gutter brooms.  Optional 11’ path available with 54” gutter brooms.  Oversized 54” brooms extend reach keeping unit a safer distance away from curbs and other obstructions.  Also helps pick-up head stay on more level road surface and away from suction breaking crowns.

- Gutter brooms are spring balanced & free floating.  They automatically apply the right surface pressure and follow surface contours for a clean sweep. They do not require costly and maintenance intensive hydraulic or pneumatic components.  No operator adjustments needed!  Spring balanced, free floating brooms lasts longer and provide a cleaner sweep.

- Standard gutter broom in cab TILT CONTROLS ensure easy broom adjustments to effectively clean deeper, hard-to-reach cutters.  This ensures better one-pass cleaning performance.

- Five separate DUST SUPPRESSION CONTROL POINTS allow operator to focus on critical dust generation areas and ensure maximum dust free sweeping performance.

- 2 spray nozzles over each gutter broom

- 4 front bumper mounted spray nozzles

- 8 at pick-up hood

- 1 at inlet tube

- 1 at intake tube

- DUST FREE SWEEPING ensured by a 3 zone, 3 electric diaphragm pump system providing up to 5.5 gpm and 200 gallon water supply.  Pumps are continuous run dry rated for longer service life.

DURABILITY AND LOWER COST OF OWNERSHIP FEATURES

- STAINLESS STEEL debris hopper and noise reducing auxiliary engine shroud are rust resistant and comes with a 5 year NO RUST THROUGH FACTORY WARRANTY.   Shroud and debris hopper are not connected.  This makes it easier, faster and more convenient to service the engine without raising an interconnected hopper/shroud system.

- The hopper is constructed of bolt together, non-magnetic stainless steel body panels which greatly reduce repair/replacement costs.  Replace a damaged panel – never the entire hopper.  Bolt together panels also eliminate the need for welds which weaken the structural integrity of the hopper and can rust.

- The R-6XL comes equipped with an over-sized Tier 4 Interim Kubota 74.3 HP turbo-diesel auxiliary engine.  It provides more than sufficient power at minimum operating speeds.  Engine has high temperature/low oil pressure auto shutdown.

- OVERSIZED 30 gallon hydraulic reservoir ensures maximum performance and minimalizes overheating risks.

- A simple electric over hydraulic valve system consists of a cast aluminum manifold with externally mounted universal fit valve bodies.  Defective valves can be replaced in 10 minutes & are interchangeable with other brands for lower costs and quick repairs.

- To make troubleshooting quicker & easier, the hydraulic system incorporates integral hydraulic pressure monitoring gauges readable from operators control panel in cab.

- Simplified wiring is housed in a NEMA Class 4 box which is “weather proof” against dust and moisture.  Numbered wiring is heat stamped on and will never wear off.   It is easier to identify versus weathered (faded or dirty) colored wiring.

- Gutter brooms are mounted to heavy duty 4” x 4” x .25” tube steel posts providing maximum support against impacts and minimizing maintenance costs.

- LED lighting produces greater illumination while consuming two thirds less power than incandescent bulbs.

- Vacuum intake tube constructed of longer lasting abrasion resistant steel.  Bolt-in design makes replacement quick, easy and very economical.

- 12 volt back-up hydraulic system operates all sweeper functions in event of engine failure.  This makes repairs fast and easy.

- Hood mounted replaceable intake & exhaust tubes are of longer wearing, abrasion resistant steel construction.

- The impeller is a turbine type with 10 blades, 30” in diameter and constructed of two abrasion resisting grades of long wearing steel.  To prevent weld or material failure, each blade is keyed to match a corresponding notch in both the front and rear plate.

- To maximize impeller fan service life, the fan housing is lined with replaceable corded rubber and held in place with abrasion resistant liner bolts.

- FLEXIBLE HOOD STOPS ensure safe and secure resting position for raised pick-up head during transit.  Prevents hood bending due to hydraulic cylinder up pressure or travel impacts.

EASE OF OPERATION & OPERATOR SAFETY FEATURES

- Mounted on a NON-CDL 26,000 GVWR chassis equipped with low profile tires, the unit provides EASIER/SAFER entry/exiting of the cab.  The lower profile also improves the operator’s forward view to the ground ahead.  Better front and side visibility often eliminates need for expensive dual steering.

- All operating controls conveniently located in cab.  Intuitive/dependable rocker switches control all functions.  Control panel vertically mounted in front of the bench seat to prevent spilled liquids from contaminating the switches.  For operator ergonomic comfort, the control box has dual action pivot points, UP - DOWN / LEFT - RIGHT, permitting operator to adjust box to better see the control switches.  A console light provided for night operation.  Large dial faces aid in effective operation.

- “EYES FORWARD” color camera safety system keeps operator facing forward versus constantly diverting attention to rear view mirrors.  Dash board mounted 7” COLOR MONITOR (positioned slightly to right of operator’s forward view) provides operator with clear view of right side broom and rear bumper.

- All Stewart-Amos sweepers are built with time tested, multi-vendor source able, off the shelf components.

- ALL LED LIGHTING means never a bad bulb.  Provides greater assurance your units is operating safely and legally.

- Large, stainless steel double access storage compartment with over 20 cubic feet of space extends across the rear of the unit.  Rakes, shovels and vacuum hose extensions are easy to store.